## Slide 1: Embedded Programming and Roboticss
Lesson 15
Bluetooth and the Raspberry Pi
bnbnbnb

## Slide 2: Bluetooth Overview
As you will recall from the Arduino, Bluetooth is a short-range wireless protocol
Bluetooth devices must be paired with each other to communicate
Setup on the Pi requires a little more work
Standard PIN code is 1234

## Slide 3: Bluetooth Tools
Download the utilities:
sudo apt-get install bluetooth bluez-utils blueman
Install the Python libraries:
sudo apt-get install python-serial

## Slide 4: Alternate Bluetooth with HC05
If you’re using an HC05 module instead of a USB-connected dongle, do the following:
Plug the HC05 into the breadboard
Connect the RX pin on the HC05 to the TX pin on the Pi and the TX pin on the HC05 to the RX pin on the Pi. TX is pin 8 and RX is pin 10
Connect Vcc and ground

## Slide 5: Alternate Bluetooth with HC05
Disable serial port on the Pi:
sudo raspi-config
Choose advanced options
Under advanced options, disable the serial port. This frees it up for your use

## Slide 6: Alternate Bluetooth with HC05
Write a Python program to receive characters
import serial
port = serial.Serial(“/dev/ttyAMA0”, baudrate=9600, timeout=8.0)
port.open()
while True:
rcv=port.readline()
print(str(rcv))

## Slide 7: Alternate Bluetooth with HC05
Similarly, you can send data to your Arduino
port.write(bytes(‘B’, “UTF-8”))
You cannot directly write strings, nor read them. You must convert to a byte stream going out, and from a byte stream coming in

## Slide 8: Alternate Bluetooth with HC05
Using the Pi as a Bluetooth master:
import serial
import time
port=serial.Serial(“/dev/ttyAMA0”, baudrate=9600, timeout=8.0)
port.open()
port.write(bytes(“abc”, “UTF-8”))
iime.sleep(5)
port.close()

## Slide 9: Using Minicom for Commands
sudo apt-get install minicom
minicom -b 9600 -o -D /dev/ttyAMA0

## Slide 10: Reference for HC05 Bluetooth on Pi
http://blog.miguelgrinberg.com/post/a-cheap-bluetooth-serial-port-for-your-raspberry-pi

## Slide 11: Bluetooth Connection
Use the hciconfig utility to get the name and address of the Bluetooth adapter:
hciconfig
Scan for available Bluetooth devices. These must be discoverable. If you have an Android phone, set it to be found, then run:
hcitool scan
You should see the name and address of available devices

## Slide 12: Bluetooth Connection
Pair with the device:
sudo bluez-simple-agent hci0 xx:xx:xx:xx:xx:xx
The hci0 is the name of the Bluetooth adapter on your Pi
The address following it is the address with which you want to pair

## Slide 13: Bluetooth Configuration
Edit the configuration file using the following:
sudo leafpad /etc/bluetooth/rfcomm.conf
Make it look like this:
rfcomm1 {
bind yes;
device xx:xx:xx:xx:xx:xx;
channel 1;
comment "Connection to Bluetooth serial module";
}

## Slide 14: Bind the Channel and Pair
sudo rfcomm bind all
Pair the Pi with the other Bluetooth device
sudo bluetoothctl
You’ll get a command prompt. Enter the address of the Arduino
command: pair xx:xx:xx:xx:xx

## Slide 15: Programming with Python
Import the Bluetooth modules:
from bluetooth import *
Constant for the Bluetooth board on the Arduino:
bd_addr = "20:14:12:02:23:95"

## Slide 16: Connect to Arduino
try:
sock=BluetoothSocket(RFCOMM)
sock.connect((bd_addr, port)) # Parentheses!
print("Initial connection")
conn = 1
except BluetoothError as bt:
print(‘Cannot connect to host' + str(bt))
exit(0)

## Slide 17: Send Something
In my home-control system, this sends a request for status information to the Arduino unit in the garage
try:
sock.send("S")
except BluetoothError as err:
print("Bluetooth error on send“ + str(err))

## Slide 18: Receive Data
The code on the following slide receives data
Note that we might not get everything at once, so this is enclosed in a loop, not shown
What we get is a byte array, which is converted to a string with the str() function

## Slide 19: Receive Data
try:
buf = sock.recv(80)
except BluetoothError as err:
print("Bluetooth error on receive")
break;
if len(buf) > 0:
datatemp = str(buf)
data = data + datatemp

## Slide 20: References
http://linuxcommand.org/man_pages/hcitool1.html

## Slide 21: Exercise
Use the Curses library
Write a program on the Pi that sends a command to the robot:
F=Forward; B=Backward; L=Left, R=Right, S=Stop
The arrow keys determine which command gets sent
On the Arduino, interpret the commands and take appropriate action
Note: if you send a command, that action will continue until you send another command. Thus sending R will cause the robot to go in a circle to the right until you send another command.

## Slide 22: Exercise
How would you add speed control?
Specifically, how would you modify the Arduino program, and what could you add to the Raspberry Pi program for this? How would you show it on the screen?
Do it.